## Slide 2: Appendices

## Slide 3: Prototype

## Slide 4: Materials used
ESP32
MAX9814 sound sensor
AD5620 Amplifier
3d printed casing
Isolation material
Jumper wires
Capacitors

## Slide 5: Prototype Development Timeline
Initial Test: Sound Sensor + Digital Filtering
Replaced Digital Filter with AI Model (Springer Algorithm)
Design of Circular Casing for Noise Cancellation
Redesigned Casing to Hexagon Based on Simulation Results (Better Noise Cancellation)
Added Isolation Layer for Improved Noise Cancellation
Added amplifier and capacitors to filter electric noise out
Tested Piezo Sensor with Custom Casing (Contact Detection)
Returned to Sound Sensor (Better Results)
Added Membrane + O-ring to Boost Heartbeat Signal
Final Setup: Sound sensor + AI model + Hexagonal casing + isolation + membrane

## Slide 6: MAX9814 vs. Piezo Sensor
Overview of MAX9814 (Air-Coupled Sensor)
Integrated microphone with built-in automatic gain control (AGC) amplifier.
Initially selected for its ease of use and real-time acoustic sensing.
An external AD5620 amplifier was tested to improve audio clarity.
Result: No significant improvement observed with external amplification.
Overview of Piezoelectric Sensor (Contact Sensor)
Operates by detecting mechanical vibrations directly from surface contact.
Designed and tested with a custom casing to optimize signal pickup.
Advantage: Immune to airborne noise
Drawback: Introduced more high-frequency electrical noise and requires additional filtering.
Conclusion
Despite the theoretical benefits of the piezo sensor in isolating environmental noise, practical testing showed higher susceptibility to electrical interference.
Therefore, the MAX9814 was selected for the final prototype.